## Slide 1: Correlation of SAR images

## Slide 2: What is SAR images?
SAR images stands for Synthetic Aperture Radar, it refers to a technique that stands for producing fine resolution images from resolution limited radar system
To create a SAR image successive pulses of radio waves are transmitted to illuminate a target pulse is received and recorded. SAR is capable of operating under inclement weather conditions day or night.

## Slide 3: Processing the SAR images
Processing of SAR data is required to extract relevant features, such as objects or buildings. Detection of such objects is based on the detection of locally bright pixels, followed by clustering of neighborhoods of pixels.
SAR remote sensing provides a new dimension for measuring various bio-geophysical parameters of the features on Earth surface.
Noise Despeckling cleans SAR images
Image fusion is a useful tool for integrating low spatial resolution multispectral (MS) images with a high spatial resolution panchromatic (PAN) image, thus producing a high resolution multispectral image for better understanding

## Slide 4: Some methods which are used to correlate SAR images.
Object Detection
Feature Matching
Cross Correlation
Sparse Representation based classification(SRC)
Feature extraction and Classification Processes

## Slide 5: OBJECT DETECTION
It is a computer vision technique for locating instances of objects in images. It uses deep learning and some methods are
CNN (Convolutional Neural Network),
RCNN(Regions with Convolutional Neural Network)
Fast R CNN,
Faster R CNN,
Histogram of Oriented gradients,
Single shot detector,
Spatial Pyramid Pooling(SPP NET),
YOLO

## Slide 6: FEATURE MATCHING
The feature matching of images can be divided into three categories: point feature matching method, line feature matching method and region feature matching method. Representative algorithms are: Scale-invariant feature transform (SIFT) method , Hough operator and Maximally Stable Extremal Regions (MSER) operator .
Feature descriptors are based on gaussian-gamma-shaped edge strength maps instead of original images. This method combines both edge features and point features to reach a match target.
The second one is SAR-SIFT algorithm, This kind of method is based on improvement of sift algorithm.

## Slide 7: Scale-invariant feature transform algorithm
The SIFT algorithm is a kind of computer vision algorithm. This algorithm detects and describes the local features in the image. It searches for local extremum points in the scale space and extracts its position, scale, and rotation invariants.
The SIFT algorithm is based on the search of different scale space to detect feature points and to determine the direction of feature points. The characteristics of the feature points found by SIFT algorithm are very prominent.
These feature points do not change due to illumination intensity, affine transformation of images, and varying degrees of interference noise.

## Slide 8: SIFT
These feature points include points such as the corner points of ground objects, the edge points of objects on the image, the bright spot in the dark area of the image, and the dark spot appearing in the bright area.
The SIFT algorithm is widely used in computer vision to match images or for local target recognition, and is suitable for various applications such as target retrieval, image retrieval, transformation, registration or image tracking

## Slide 9: SAR-SIFT: A SIFT-LIKE ALGORITHM FOR SAR IMAGES
The SAR-SIFT algorithm is an operator that extracts local features from SAR images and performs feature description.
This algorithm has potential applications for all image comparison applications that require stability and invariance, including matching, change detection and template-based target detection. In this method a new SAR-Harris feature point detection method.
The SAR-Harris feature detection method uses multi-scale SAR-Harris matrix and multi-scale SAR-Harris function to calculate the multi-scale results of the original image, thus replacing the scale space in the SIFT algorithm.

## Slide 10: SAR-SIFT
The feature points acquired by the SAR-Harris feature detection method are mostly located at the corners or bright spots of the image. The SAR-SIFT algorithm also proposes to apply fuzzy Gaussian functions with different weights in different directions of SAR images. Using the ratio of average ratio (ROA) .
A new gradient calculation method named Gradient by Ratio (GR) is defined. The GR histogram is used to calculate the gradient histogram and gradient direction of the SAR image, so that the detected feature points are characterized and the corresponding ratio feature descriptors are obtained. (Ratio Descriptor).

## Slide 11: Hough line detection algorithm
Hough line detection algorithm is mainly used to extract geometric shapes (such as lines, circles, etc.) with certain identical features from the image.
The basic principle is to use the point-to-line duality to convert the curve in the original image space to a point in the parameter space. The points of the collinearity in the image plane space correspond to the lines intersecting in the feature space.
Correspondingly, all the lines intersecting at the same point in the parameter space have collinear points corresponding to them in the image plane space.

## Slide 12: Hough line detection algorithm
Therefore, the Hough line detection algorithm converts the line detection problem in the image plane space into the detection problem of the points in the feature space, and completes the detection task by performing simple accumulation statistics in the feature space.
The Hough line detection algorithm has strong anti-interference ability and is not sensitive to noise in images. However, the time complexity and space complexity of the algorithm are high, and the length information of the line segment is lost during the transformation process

## Slide 13: Maximally stable extremal regions algorithm
The Maximally stable extremal regions algorithm (MSER) is a method for performing spot detection in images.
Based on the concept of watershed, the MSER algorithm performs binarization on a grayscale image (the gray value is 0~255), and the threshold is incremented from 0 to 255.
In all of the binary images obtained, some of the connected regions in the image change little or even without change, and the region is called the maximum stable extremum region.
MSER has the invariance of affine transformation on image gradation, and multi-scale detection can be realized without any smoothing processing, that is, small and large structures can be detected.

## Slide 14: Feature matching for SAR and optical images based on gaussian-gamma-shaped edge strength map
The method proposes to eliminate the overall rotation deviation and resolution difference between images after image coarse correction.
After logarithmically transforming the SAR image, the method uses phase consistency feature point extraction method to obtain robust noise suppression. Feature points.
Based on this, the method uses on the Gaussian-Gamma-shaped (GGS) bilateral window operator and obtains the edge intensity map of SAR images and optical images based on two images.
SIFT feature description based on edge intensity maps of two images. Finally, the matching process between the SAR image and the optical image is completed based on the constraints of the image geometric condition.

## Slide 15: Matching SAR and optical images using modified hausdorff distance and genetic algorithms
This method performs matching of SAR and optical images by using edge features.
Considering the coherent noise interference of SAR image, the SAR image is subjected to logarithmic transformation preprocessing, and the canny edge feature map of the preprocessed SAR image is extracted, the Canny edge feature map is directly extracted from the optical image.
Based on the Canny edge feature, the method uses genetic algorithm to search the template of the image, and calculates the modified hausdorff distance of SAR and optical images to complete the feature matching.

## Slide 16: Cross Correlation
Normalized Cross Correlation (NCC) for Synthetic Aperture Radar (SAR) image matching.
The main drawbacks of the NCC algorithm are the flatness of the similarity measure maxima, due to the self-similarity of the images, and the high computational complexity [1].
To tackle these two problems, we adopt the block partitioning strategy, texture feature analysis, and the Fast Fourier Transformation (FFT) algorithm and Integral Images to improve the performance of the conventional NCC algorithm.

## Slide 17: Sparse Representation based classification(SRC)
We propose a sparse representation approach for classifying different targets in Synthetic Aperture Radar (SAR) images.
Unlike the other feature based approaches, the proposed method does not require explicit pose estimation or any preprocessing. The dictionary used in this setup is the collection of the normalized training vectors itself.
Computing a sparse representation for the test data using this dictionary corresponds to finding a locally linear approximation with respect to the underlying class manifold.

## Slide 18: SRC
SAR images obtained from the Moving and Stationary Target Acquisition and Recognition (MSTAR) public database were used in the classification setup. Results show that the performance of the algorithm is superior to using a support vector machines based approach with similar assumptions.
Significant complexity reduction is obtained by reducing the dimensions of the data using random projections for only a small loss in performance.

## Slide 19: Feature extraction and Classification Processes
The performance of two feature extraction techniques are analyzed with respect to classification. Image analysis is limited by the inherent noise present in SAR images, known as speckle.
Preprocessing is necessary to remove the speckle noise. For this purpose, Lee filter is applied on the image. For feature extraction spectral based methods are used.
Among them, Laws mask and Gabor filter based feature extraction techniques are used here. Laws mask is a bank of filters, that is appropriate for texture identification, gabor filter is a linear filter used to represent and to discriminate texture features.
The extracted features are grouped into different classes using classification techniques such as the k-means and fuzzy c means (FCM) clustering and are two unsupervised classification techniques